## Slide 1
PROJECT DETAILS |  |  |  |  |  |  |  |  | 
NAME: 3-Bedroom Detached House Show Home |  |  |  | SITE ADDRESS: <site address> |  |  |  | CLIENT NAME: <client name> | 
CONTRACTOR DETAILS |  |  |  | 
NAME: <contractor’s name> | ADDRESS: <contractor’s address > | PHONE |  | E-MAIL: <contractor’s e-mail>
 |  | office: <###> | mobile: <###> | 
GENERAL INSTRUCTIONS and PREPATORY NOTES | 
1/ | Please review this specification, the reference drawings and schedules and contact me as soon as possible with any issues or questions.
2/ | A separate document section is provided for each flooring type (sections 2-7), specifying all product details and their room/area’s designation(s).
3/ | All floor transition details are provided in the last section (8) of this specification.
4/ | No substitutions are to be made unless agreed upon ahead of time.
5/ | Important scheduling note: The Kährs wood floors must not be laid until all other work, e.g. painting, wallpapering and tiling, is completed. The site must have the correct RH (relative humidity) which is below 60% during installation to avoid soiling and moisture damage to the floor.
6/ | Acclimatization of products (These are only the main considerations, for more details please refer to the relevant installation guides): Before installing the Kährs engineered flooring, it must be ensured that the material has a minimum temperature of 18°C. To stop the floor absorbing moisture prior to installation, it is important not to open packaging until just before installation. (See section 2) The Tarkett vinyl sheet flooring must be stored in the room where it is to be laid for at least 24 hours beforehand, to allow it to adapt to a temperature of 18°C or more during laying. (See section 3) Harvey Maria vinyl tile flooring should be stored in piles together with the adhesive in the relevant room for at least 24 hours prior to fitting in order to acclimatize to the conditions of the room [the ambient temperature should be at least 18ºC / sub-floor temperature at least 15ºC]. (See section 4) All Polyflor products must be conditioned for at least 24 hours prior to installation. (See Section 5)
7/ | Please prepare all surfaces appropriately, including any necessary repairs.
8/ | The specific manufacturer’s installation instructions are to be followed in each case.
9/ | Laying directions are evident on the referenced drawings and any further clarifying instructions are included in the specification tables.
10/ | As much as possible, please leave the work areas in a tidy fashion at the end of each day. All rubbish is to be promptly removed from the site.
MAIN DETAILS

## Slide 2
PRODUCT DETAILS |  |  |  |  |  |  | 
ITEM TYPE | BRAND / SUPPLIER | NAME | CODE / REF | DIMS per UNIT (mm) | COLOUR | OTHER SPECIFICS | INSTALLATION NOTES and WWW LINKS
Engineered Hardwood Planks | Kährs | Hard Maple Edmonton | 152N55AP50KW 0 | 15D x 200W x 2423L | Cream White to Golden Cream | Wood Species: Hard Maple Design: 2-strip Grading: City Joint type : Woodloc® 5S Surface treatment: Silk matt lacquer | To be installed floating on a level, solid surface such as concrete, particleboard or wood. Can also be glued down. Installation instructions and data sheets from manufacturer at: http://www.kahrs.com/en/Builders/Products/Floors/Kahrs-Original/American-Naturals-Collection/Hard-Maple-Edmonton/ (Please see Tab Installation & Maintenance for document links.)
ACCESSORIES |  |  |  |  |  |  | 
Stairnose | Kährs | Solid Woodloc® Stairnose | 7028012AP50 | 60W x 35H | Cream White to Golden Cream | Wood Species: Hard Maple Surface treatment: Silk matt lacquer | Apply where the floor reaches a step down (staircase between ground and first floor). Locks into floor using Woodloc® joint.
Skirting | Skirtech | Small Bullnose | Code: SMB ID: 44 | 18D x 70H x 3050L | N/A –paintable | Primed option Material: MDF | Product info at: http://www.skirtech.co.uk/Small_Bullnose_MDF_695--product--44.html
ENGINEERED HARDWOOD FLOORING
Section 2 Engineered Hardwood Flooring continued on next page: Designation on Site Details …

## Slide 3
ENGINEERED HARDWOOD FLOORING – continued
 | DESIGNATION ON SITE DETAILS |  |  | 
# | ROOM/AREA | Ref ID within room | FLOOR AREA (estimated, m2) | REFERENCE DRAWING
1 | Hall | 1 | 9.24 [12.16 (outside perimeter area) – 2.93 (area of staircase tread projection on floor)] | (D3) Flooring – Ground Floor
2 | Stairs | 1 | 5.7 [3.2 (tread) + 2.5 (rise)] | (D3) Flooring – Ground Floor, (D4) Flooring – First Floor
3 | Landing | 1 | 6.47 | (D4) Flooring – First Floor
4 | Study | 1 | 7 | (D3) Flooring – Ground Floor
5 | Sitting Room | 1 | 17.48 | (D3) Flooring – Ground Floor
6 | Playroom | 1 | 9.5 | (D3) Flooring – Ground Floor
7 | Dining Room | 1 | 15.54 | (D3) Flooring – Ground Floor
8 | Kitchen | 1 | 14.44 | (D3) Flooring – Ground Floor
9 | Children’s Room | 1 | 13.3 | (D4) Flooring – First Floor
10 | Guest Room | 1 | 13.3 | (D4) Flooring – First Floor
11 | Master Bedroom | 1 | 32.34 | (D4) Flooring – First Floor
 |  |  | TOTAL (estimated): 144.31 | 

## Slide 4
PRODUCT DETAILS |  |  |  |  |  |  | 
ITEM TYPE | BRAND / SUPPLIER | NAME | CODE / REF | DIMS per UNIT (mm) | COLOUR | OTHER SPECIFICS | INSTALLATION NOTES and WWW LINKS
Vinyl Sheet | Tarkett | Akira/White, Design 260 | 5518063 | 2.6 thickness Roll W=200 Min 3500 sheet length is required | White & Grey melange | Adhesive: TarkoSpray | Detailed installation instructions at: http://home.tarkett.com/products/vinyl/design/design-260#nav-tab-6 (Please download the first document on the list.) Detailed information on how to use TarkoSpray adhesive at: http://home.tarkett.com/products/accessories/vinyl-adhesives/tarkospray
ACCESSORIES |  |  |  |  |  |  | 
Wall base | N/A – Vinyl wall panels will serve as a wall base (to be installed by the Decorator). |  |  |  |  |  | 
VINYL SHEET FLOORING
DESIGNATION ON SITE DETAILS |  |  | 
ROOM/AREA | Ref ID within room | FLOOR AREA (estimated, m2) | REFERENCE DRAWING
Downstairs Bathroom | 1 | 5.95 | (D3) Flooring – Ground Floor

## Slide 5
PRODUCT DETAILS |  |  |  |  |  |  | 
ITEM TYPE | BRAND / SUPPLIER | NAME | CODE / REF | DIMS per UNIT (mm) | COLOUR | OTHER SPECIFICS | INSTALLATION NOTES and WWW LINKS
Vinyl Tile | Harvey Maria | Luxury Vinyl Tile | N/A | 305W x 305L x 2.5T (tile) | Latte White | Adhesive: Harvey Maria Regular No grout is required. | Installation instructions at: http://www.harveymaria.co.uk/Fitting-Care/For-the-Home Product details link: http://www.harveymaria.co.uk/Floor-Range/LSI-Solid-Colours_2/Latte-White Adhesive details and instructions at: http://www.harveymaria.co.uk/Floor-Range/Fitting-and-Care/Recommended-Adhesive Sealing note: The tiles will bond with the adhesive to form a water-tight seal. Small gaps at the edges of the room, at the shower tray, around the toilet and sink bases etc. are to be filled with a mastic sealant.
ACCESSORIES |  |  |  |  |  |  | 
Skirting | Polyflor | Ejecta Sit-on Skirting | MC14, For Black Colour - 9510 | 75H x 20W (section on floor) x 2T, available in 2000 lengths. | Black | For more detailed product specification: http://www.polyflor.com/jh/products.nsf/products!open&prodcode=ejecta (Please see Sit-on skirting PDF file) | Installation instructions at: http://www.polyflor.com/jh/products.nsf/products!open&prodcode=ejecta (Please see Flooring Accessories Installation PDF file.) Suitable Mastic Sealant is to be used beneath the toe of the skirting.
VINYL TILE FLOORING (Harvey Maria)
DESIGNATION ON SITE DETAILS |  |  | 
ROOM/AREA | Ref ID within room | FLOOR AREA (estimated, m2) | REFERENCE DRAWING
Shower Room | 1– Vinyl tiles 2 -- Skirting | 5.28 | (D4) Flooring – First Floor

## Slide 6
PRODUCT DETAILS |  |  |  |  |  |  | 
ITEM TYPE | BRAND / SUPPLIER | NAME | CODE / REF | DIMS per UNIT (mm) | COLOUR | OTHER SPECIFICS | INSTALLATION NOTES and WWW LINKS
Vinyl Tile | Polyflor | Camaro Stone and Design PU Luxury Vinyl Tile | 2317 | 305W x 305L x 2T (tile) | Black Marble | For more detailed product specification: http://www.polyflor.com/jh/web.nsf/technical!open&section=Product%20Specifications (Please see Camaro Stone and Design PU PDF file.) | Installation instructions at: http://www.polyflor.com/jh/web.nsf/technical!open&section=Installation (Please see LVT Technical Manual, Subfloor Preparation, Installation of Luxury Vinyl Tiles, Type of Adhesives, Tools and Equipment PDF files.) Please use adhesive only from the Approved Adhesive list: http://www.polyflor.com/jh/web.nsf/technical!open&section=Approved%20Adhesive%20List
ACCESSORIES |  |  |  |  |  |  | 
Grouting Strips | Polyflor | Ice Grouting Strip | 2031 | 3W x 914L x 2T | Ice | For further details: http://www.polyflor.com/jh/products.nsf/products!open&family=lux&prodcode=csd&shade=2031 | Installation instructions at: http://www.polyflor.com/jh/web.nsf/technical!open&section=Installation (Please see LVT Technical Manual, LVT Inlay Strip Calculation Sheet PDF files.)
Skirting | Polyflor | Ejecta Sit-on Skirting | MC14, For White Colour – 9520 | 75H x 20W (section on floor) x 2T, available in 2000 lengths. | White | For more detailed product specification: http://www.polyflor.com/jh/products.nsf/products!open&prodcode=ejecta (Please see Sit-on skirting PDF file) | Installation instructions at: http://www.polyflor.com/jh/products.nsf/products!open&prodcode=ejecta (Please see Flooring Accessories Installation PDF file.) Suitable Mastic Sealant is to be used beneath the toe of the skirting.
VINYL TILE FLOORING (Polyflor)
DESIGNATION ON SITE DETAILS |  |  | 
ROOM/AREA | Ref ID within room | FLOOR AREA (estimated, m2) | REFERENCE DRAWING
Ensuite Bathroom | 1 | 8.32 | (D4) Flooring – First Floor

## Slide 7
PRODUCT DETAILS |  |  |  |  |  |  | 
ITEM TYPE | BRAND / SUPPLIER | NAME | CODE / REF | DIMS per UNIT (mm) | COLOUR | OTHER SPECIFICS | INSTALLATION NOTES and WWW LINKS
Outdoor Deck Tiles | Kandy Outdoor Flooring | Granite Outdoor Deck Tiles | BD-GRAN-3X-SB | 300 x 300 (tile) Tile height: 30 Base height: 16 Granite thickness: 12 | Light Grey | Surface finish: hammered anti-slip | No grout and no adhesive are needed. The tiles are to be simply laid on top of the existing surface. Inbuilt tabs are used to connect the tiles to each other. Product info and spec: http://outdoorflooring.ca/portfolio/granite/ http://outdoorflooring.ca/wp/wp-content/uploads/2013/05/9031.pdf
ACCESSORIES |  |  |  |  |  |  | 
N/A |  |  |  |  |  |  | 
OUTDOOR DECK TILES
DESIGNATION ON SITE DETAILS |  |  | 
ROOM/AREA | Ref ID within room | FLOOR AREA (estimated, m2) | REFERENCE DRAWING
Patio | 1 | 15.4 | (D3) Flooring – Ground Floor

## Slide 8
PRODUCT DETAILS |  |  |  |  |  |  | 
ITEM TYPE | BRAND / SUPPLIER | NAME | CODE / REF | DIMS per UNIT (mm) | COLOUR | OTHER SPECIFICS | INSTALLATION NOTES and WWW LINKS
Polypropylene Tiles | Bergo Flooring | Bergo XL Nature | 110SR30 | 377.2 x 377.2 (tile) Thickness 10.1 | Spring Grass (green) | Environmentally friendly recyclable UV- stabilized polypropylene. | No special tools, glue or screws are required. Tapping a rubber mallet or similar over the protruding rings easily interlocks the tiles together. Please see below for more details. Installation instructions: http://www.bergoflooring.com/en/home/installation-instruction/ (Please select Installation Instructions for System 2 PDF and Video for Bergo Floor System 2) Product info: http://www.bergoflooring.com/en/home/products/bergo-xl/ (See Nature)
ACCESSORIES |  |  |  |  |  |  | 
N/A |  |  |  |  |  |  | 
POLYPROPYLENE TILES
DESIGNATION ON SITE DETAILS |  |  | 
ROOM/AREA | Ref ID within room | FLOOR AREA (estimated, m2) | REFERENCE DRAWING
Balcony | 1 | 15.4 | (D4) Flooring – First Floor

## Slide 9
PRODUCT DETAILS (Interior Door thresholds only) |  |  |  |  |  |  | 
ITEM TYPE | BRAND / SUPPLIER | NAME | CODE / REF | DIMS per UNIT (mm) | COLOUR | OTHER SPECIFICS | WWW LINKS
Transition strip | Kährs | Solid Bevel Cover Strip | 7026024AP50 | 58W x 20D, Length per door width | Cream White to Golden Cream | Wood Species: Hard Maple Surface treatment: Silk matt lacquer | This level moulding is used for making a smooth transition between floors of differing heights. Product details at: http://www.kahrs.com/Templates/Kahrs/Pages/ProductMouldingPage.aspx?id=13483&epslanguage=en Comes with a track system for easy installation.
FLOOR TRANSITIONS
DESIGNATION ON SITE DETAILS (Interior Door thresholds only) |  | 
THRESHOLD AT | DOOR OPENING WIDTH (mm) | REFERENCE DRAWING
Door between Hall and Downstairs Bathroom | 800 | (D3) Flooring – Ground Floor
Door between Landing and Shower Room | 800 | (D4) Flooring – First Floor
Door between Master Bedroom and Ensuite Bathroom | 800 | (D4) Flooring – First Floor
Exterior Doors THRESHOLDS For the following thresholds at the exterior doors, please select appropriate transition solutions according to each particular doorstep situation. Please ensure proper weatherproofing. The solution does not need to involve Kährs transition strip products necessarily. Please ensure any proposed solutions are coordinated and agreed upon prior to installation. |  | 
THRESHOLD AT | DOOR OPENING WIDTH (mm) | REFERENCE DRAWING
Main Entrance into Hall | 850 | (D3) Flooring – Ground Floor
Door between Kitchen and Patio | 850 | (D3) Flooring – Ground Floor
Door between Master Bedroom and Balcony | 800 | (D4) Flooring – First Floor