## Slide 1
PROJECT DETAILS |  |  |  |  |  |  |  |  | 
NAME: 3-Bedroom Detached House Show Home |  |  |  | SITE ADDRESS: <site address> |  |  |  | CLIENT NAME: <client name> | 
CONTRACTOR DETAILS |  |  |  | 
NAME: <contractor’s name> | ADDRESS: <contractor’s address > | PHONE |  | E-MAIL: <contractor’s e-mail>
 |  | office: <###> | mobile: <###> | 
GENERAL INSTRUCTIONS and PREPATORY NOTES | 
1/ | Please review this specification, the reference drawings and schedules and contact me as soon as possible with any issues or questions.
2/ | This specification is organized in a room-by-room format (a separate section is provided for each area).
3/ | Important scheduling note for coordination with the flooring contractors: The Kährs wood floors cannot not be laid until all other work, e.g. painting, wallpapering and tiling, is completed. After the Kährs wood floors have been laid and the paintable skirting boards installed, the painters must return to paint them per the specification tables.
4/ | No substitutions are to be made unless agreed upon ahead of time.
5/ | Please prepare all surfaces appropriately, including any necessary repairs to walls and woodwork.
6/ | The specific manufacturer’s instructions are to be followed in each case.
7/ | As much as possible, please leave the work areas in a tidy fashion at the end of each day. All rubbish is to be promptly removed from the site.
MAIN DETAILS

## Slide 2
TYPE OF SURFACE | PRODUCT DETAILS |  |  |  |  |  |  |  | 
 | Ref ID within room | TYPE | BRAND / SUPPLIER | NAME | CODE / REF | COLOUR | FINISH | REFERENCE DRAWING and WALL IDENTIFIER(S) | ADDITIONAL INFO and WWW LINKS
Walls | -- | Paint, Water-based | Dulux | Dulux Lifemaster Zero VOC | 50YY 83/029 Natural White | Off-white | Eggshell | (D5) Painter/Decorator/Installer – Ground Floor (D6) Painter/Decorator/Installer – First Floor All walls, including staircase | http://www.dulux.ca Please use Dulux brand primer appropriate for the condition of the surface, preferably the zero VOC Lifemaster.
Ceilings | -- | Paint, Water-based | Dulux | Dulux Lifemaster Zero VOC | Ceiling Flat | Standard White (Untinted) | Flat | - | 
Skirtings | -- | Paint, Water-based | Dulux | Dulux Lifemaster Zero VOC | 50YY 83/029 Natural White | Off-white | Semi-Gloss | - | 
Woodwork (including built-in under-stairs storage cabinets) | -- | Paint, Water-based | Dulux | Dulux Lifemaster Zero VOC | 50YY 83/029 Natural White | Off-white | Semi-Gloss | - | 
HALL, STAIRS AND LANDING
Note: For the mirrored wall sections as marked on the (D1) Furnishing Layout - Ground Floor and (D2) Furnishing Layout - First Floor drawings, full wall height standard mirrors are to be installed after all other wall and ceiling finishes are applied. To measure for ordering: (1) Full wall height is to be measured from top edge of skirting to ceiling; (2) Please obtain exact widths according to each particular description given on the relevant furnishing layout drawing. (Generally, each wall section in these 3 areas is to be measured from edge/corner to edge/corner, as shown on the floor plan.) Please also see (D5) Painter/Decorator/Installer - Ground Floor and (D6) Painter/Decorator/Installer - First Floor drawings for wall sectioning reference.

## Slide 3
TYPE OF SURFACE | PRODUCT DETAILS |  |  |  |  |  |  |  | 
 | Ref ID within room | TYPE | BRAND / SUPPLIER | NAME | CODE / REF | COLOUR | FINISH | REFERENCE DRAWING and WALL IDENTIFIER(S) | ADDITIONAL INFO and WWW LINKS
Walls | -- | Paint, Water-based | Dulux | Dulux Lifemaster Zero VOC | 10BB 83/006 Atmosphere | Off-white | Eggshell | (D5) Painter/Decorator/Installer – Ground Floor All walls not marked. | http://www.dulux.ca Please use Dulux brand primer appropriate for the condition of the surface, preferably the zero VOC Lifemaster.
 | 2 | Wallpaper | Galerie / Fabrics & Papers | Deauville Open Stripe Wallpaper | G23067 | Taupe stripe wallpaper, with narrow navy stripe on off white | - | (D5) Painter/Decorator/Installer – Ground Floor Wall S1 | Width: 53cm, Roll length: 10m, Pattern Repeat: 0cm, Design Repeat: Free. Washable; Peel-able; Lightfast; Paste the Wall. Stripes orientation: horizontal http://www.galeriehome.co.uk/international/php/main.php http://www.fabricsandpapers.com/item/view/8420-deauville-open-stripe-wallpaper
Ceiling |  | Paint, Water-based | Dulux | Dulux Lifemaster Zero VOC | Ceiling Flat | Standard White (Untinted) | Flat | - | http://www.dulux.ca Please use Dulux brand primer appropriate for the condition of the surface, preferably the zero VOC Lifemaster.
Skirtings |  | Paint, Water-based | Dulux | Dulux Lifemaster Zero VOC | 10BB 83/006 Atmosphere | Off-white | Semi-Gloss | - | 
Woodwork |  | Paint, Water-based | Dulux | Dulux Lifemaster Zero VOC | 10BB 83/006 Atmosphere | Off-white | Semi-Gloss | - | 
STUDY

## Slide 4
TYPE OF SURFACE | PRODUCT DETAILS |  |  |  |  |  |  |  | 
 | Ref ID within room | TYPE | BRAND / SUPPLIER | NAME | CODE / REF | COLOUR | FINISH | REFERENCE DRAWING and WALL IDENTIFIER(S) | ADDITIONAL INFO and WWW LINKS
Walls | 2 | Wallpaper | Eco Wallpaper / Wallpaper Direct | Graphic | 1558 | Brown | - | (D5) Painter/Decorator/Installer – Ground Floor All walls – from height 1120 mm all the way up to the ceiling (100 mm extra length is allocated for overlap under panels.) | All wallpaper must be installed before the vinyl panels (which are to slightly cover the bottom end of the wallpapered sections for a seamless look). Product info: http://www.eco.se/en/collection-graphic/wallpaper-1558/ http://www.wallpaperdirect.com/products/eco-wallpaper/eco-graphic/89917 Width 0.53 m; Roll length 10.05 m; Pattern repeat 0.18 m; Paste the wall.
 | 3 | Vinyl Wall Panels | MirroFlex / Elegant Ceilings & Walls | MirroFlex Rib 2 4FT X 8FT | N/A | White | Glossy | (D5) Painter/Decorator/Installer – Ground Floor All walls – from the floor up, height 1220 mm (4FT) | The panels are to be glued to the wall using adhesive For adhesive guidelines please see the installation instructions below. Edge J-trims (provided by the manufacturer, in white) are to be used to finish the top and bottom ends of the panels. This kind of trim simply slides onto a cut edge of the panel. Both top and bottom J-trims are to be glued to the wall. The bottom side of the J-trim that is to rest on floor is to be sealed using mastic sealer. Inside Corners (provided by the manufacturer, in matching finish) are to be used to connect the panels at the corners of the room. Manufacturer’s installation instructions: http://advtechnology.com/resource-center/install (Please select MirroFlex Structures Installation Instructions) Product info: http://www.ceilingsandwalls.com/Browse/Product/96/50/Mirroflex-Rib-2-Wall-Panel-4ft-x-8ft Accessories info: http://advtechnology.com/mirroflex/accessories/
Ceiling | -- | Paint, Water-based | Dulux | Dulux, Kitchen & Bath | 30 GG 83/006 Raindrops | Off-white | Eggshell | - | http://www.dulux.ca Please use Dulux brand primer appropriate for the condition of the surface, preferably the zero VOC Lifemaster.
Woodwork | -- | Paint, Water-based | Dulux | Dulux, Kitchen & Bath | 30 GG 83/006 Raindrops | Off-white | Semi-Gloss | - | 
DOWNSTAIRS BATHROOM
Note: For the mirrored wall section as marked on drawing (D1) Furnishing Layout - Ground Floor, full wall height standard mirror is to be installed after all other wall and ceiling finishes are applied.
To measure for ordering: (1) Full wall height is to be measured from floor to ceiling; (2) Please obtain an exact width to align with the Modernica Museum bench length when in its correct position in the bathroom corner as shown on the relevant furnishing layout drawing. Please account for the thickness of the wall panels’ J-trims when attaching to the wall. Please also see (D5) Painter/Decorator/Installer - Ground Floor drawing for wall sectioning reference.

## Slide 5
TYPE OF SURFACE | PRODUCT DETAILS |  |  |  |  |  |  |  | 
 | Ref ID within room | TYPE | BRAND / SUPPLIER | NAME | CODE / REF | COLOUR | FINISH | REFERENCE DRAWING(S) and WALL IDENTIFIER(S) | ADDITIONAL INFO and WWW LINKS
Walls | -- | Paint, Water-based | Dulux | Dulux, Lifemaster Zero VOC | 50RB 83/005 Winter Hills | Off-white | Eggshell | (D5) Painter/Decorator/Installer – Ground Floor All walls | http://www.dulux.ca Please use Dulux brand primer appropriate for the condition of the surface, preferably the zero VOC Lifemaster. All walls need to be painted and allowed to dry completely before the other 2 wall treatments can be applied.
 | 3 | Wall Sticker | Ferm Living / Modern Karibou | Powerpole | N/A | Black | - | (D5) Painter/Decorator/Installer – Ground Floor Wall SR1-VD Please see drawings (D9) Sitting Room Elevation SR1 and (D10) Sitting Room Elevation SR2 for placement on walls. | “Pole” to be positioned as shown on Sitting Room Elevation SR1. Bottom of “pole” at top edge of skirting board; “cables” to extend in both directions as illustrated: to the end of Wall SR1 to the right, and onto Wall SR2 to the left until the ceiling is reached. Installation instructions and info: http://www.modernkaribou.ca/p-1335-ferm-living-wall-sticker-powerpole.aspx
 | 4 | 3-D Wall Panels | WallArt Wall Decor | Splashes | N/A | White | - | (D5) Painter/Decorator/Installer – Ground Floor Wall SR2-VD Please see drawing Sitting Room Elevation SR2 for exact placement on wall. | Single panel size: 500 x 500 mm Eight panels are to be installed next to each other in two rows of four as shown on Elevation Drawing SR1. Manufacturer’s installation instructions and spec: http://walldecor3d.com/index.php?p=installation Product info: http://walldecor3d.com/index.php?p=onzedesigns_details&id=36
Ceiling |  | Paint, Water-based | Dulux | Dulux, Lifemaster Zero VOC | Ceiling Flat | Standard White (Untinted) | Flat | - | http://www.dulux.ca Please use Dulux brand primer appropriate for the condition of the surface, preferably the zero VOC Lifemaster.
Skirtings |  | Paint, Water-based | Dulux | Dulux, Lifemaster Zero VOC | 50RB 83/005 Winter Hills | Off-white | Semi-Gloss | - | 
Woodwork |  | Paint, Water-based | Dulux | Dulux, Lifemaster Zero VOC | 50RB 83/005 Winter Hills | Off-white | Semi-Gloss | - | 
SITTING ROOM

## Slide 6
TYPE OF SURFACE | PRODUCT DETAILS |  |  |  |  |  |  |  | 
 | Ref ID within room | TYPE | BRAND / SUPPLIER | NAME | CODE / REF | COLOUR | FINISH | REFERENCE DRAWING and WALL IDENTIFIER(S) | ADDITIONAL INFO and WWW LINKS
Walls | -- | Paint, Water-based | Dulux | Dulux, Lifemaster Zero VOC | 81YY 87/031 Fencepost | Off-white | Eggshell | (D5) Painter/Decorator/Installer – Ground Floor All walls not marked. | http://www.dulux.ca Please use Dulux brand primer appropriate for the condition of the surface, preferably the zero VOC Lifemaster.
 | 3 | Chalkboard Paint | Dynamic / Opus | - | - | Black | - | (D5) Painter/Decorator/Installer – Ground Floor Wall P1-A (This is not a full wall; please see the reference drawing for exact dimensions.) | Please apply an undercoat of black paint (Dulux 00NN 00/000) using horizontal strokes. Product info: https://store.opusartsupplies.com/sagro/storefront/store.php?mode=showproductdetail&product=36499
 | 4 | Wallpaper | Graham & Brown | Frames | 52050 | Black and White | - | (D5) Painter/Decorator/Installer – Ground Floor Wall P1-B (This is not a full wall; please see the reference drawing for exact dimensions.) | Paste the paper. Product info: http://www.grahambrown.ca/us/product/52050/Frames+%3A+Black+%26+White+Wallpaper Width: 0.52 m Length: 10 m Design match: Free
Ceiling | -- | Paint, Water-based | Dulux | Dulux, Lifemaster Zero VOC | Ceiling Flat | Standard White (Untinted) | Flat | - | http://www.dulux.ca Please use Dulux brand primer appropriate for the condition of the surface, preferably the zero VOC Lifemaster.
Skirtings | -- | Paint, Water-based | Dulux | Dulux, Lifemaster Zero VOC | 81YY 87/031 Fencepost | Off-white | Semi-Gloss | - | 
Woodwork | -- | Paint, Water-based | Dulux | Dulux, Lifemaster Zero VOC | 81YY 87/031 Fencepost | Off-white | Semi-Gloss | - | 
PLAYROOM

## Slide 7
TYPE OF SURFACE | PRODUCT DETAILS |  |  |  |  |  |  |  | 
 | Ref ID within room | TYPE | BRAND / SUPPLIER | NAME | CODE / REF | COLOUR | FINISH | REFERENCE DRAWING and WALL IDENTIFIER(S) | ADDITIONAL INFO and WWW LINKS
Walls | -- | Paint, Water-based | Dulux | Dulux, Lifemaster Zero VOC | 82YY 85/038 Belgium Lace | Off-white | Eggshell | (D5) Painter/Decorator/Installer – Ground Floor All walls not marked. | http://www.dulux.ca Please use Dulux brand primer appropriate for the condition of the surface, preferably the zero VOC Lifemaster.
 | 2 | Paint, Water-based | Dulux | Dulux, Lifemaster Zero VOC | 90YY 83/143 Spring Blossom | Pale Yellow | Eggshell | (D5) Painter/Decorator/Installer – Ground Floor Walls DR1 & DR2 | 
Ceiling | -- | Paint, Water-based | Dulux | Dulux, Lifemaster Zero VOC | Ceiling Flat | Standard White (Untinted) | Flat | - | 
Skirtings | -- | Paint, Water-based | Dulux | Dulux, Lifemaster Zero VOC | 82YY 85/038 Belgium Lace | Off-white | Semi-Gloss | - | 
Woodwork | -- | Paint, Water-based | Dulux | Dulux, Lifemaster Zero VOC | 82YY 85/038 Belgium Lace | Off-white | Semi-Gloss | - | 
DINING ROOM

## Slide 8
TYPE OF SURFACE | PRODUCT DETAILS |  |  |  |  |  |  |  | 
 | Ref ID within room | TYPE | BRAND / SUPPLIER | NAME | CODE / REF | COLOUR | FINISH | REFERENCE DRAWING and WALL IDENTIFIER(S) | ADDITIONAL INFO and WWW LINKS
Walls | -- | Paint, Water-based | Dulux | Dulux, Kitchen & Bath | 03YY 86/04 Quiet Solitude | Off-white | Eggshell | (D5) Painter/Decorator/Installer – Ground Floor All walls not marked, and walls K1 & K2 (See note below) | http://www.dulux.ca Please use Dulux brand primer appropriate for the condition of the surface, preferably the zero VOC Lifemaster. The walls are to be painted and allowed to dry completely prior to any kitchen installations, incl. the kitchen backsplash.
 | 2 | Wallpaper | Prime Walls | Motion Noise | 46624 | Red on Cream | - | (D5) Painter/Decorator/Installer – Ground Floor Wall K3 | Paste the wall. Width: 0.53 m Length: 10.05 m Design match: Straight Pattern repeat: 0.64 m Product info: http://www.primewalls.com/residential-wallpapers/viewsku/732
Ceiling | -- | Paint, Water-based | Dulux | Dulux, Kitchen & Bath | 03YY 86/04 Quiet Solitude | Off-white | Eggshell | - | http://www.dulux.ca Please use Dulux brand primer appropriate for the condition of the surface, preferably the zero VOC Lifemaster.
Skirtings | -- | Paint, Water-based | Dulux | Dulux, Kitchen & Bath | 03YY 86/04 Quiet Solitude | Off-white | Semi-Gloss | - | 
Woodwork | -- | Paint, Water-based | Dulux | Dulux, Kitchen & Bath | 03YY 86/04 Quiet Solitude | Off-white | Semi-Gloss | - | 
KITCHEN
Note: Wall IDs K1-VD and K2-VD as marked on (D5) Painter/Decorator/Installer – Ground Floor show estimated backsplash positioning along walls K1 and K2 (more details in Kitchen Fitters Specification and drawings (D11) Kitchen Elevation K1, (D12) Kitchen Elevation K2).

## Slide 9
TYPE OF SURFACE | PRODUCT DETAILS |  |  |  |  |  |  |  | 
 | Ref ID within room | TYPE | BRAND / SUPPLIER | NAME | CODE / REF | COLOUR | FINISH | REFERENCE DRAWING and WALL IDENTIFIER(S) | ADDITIONAL INFO and WWW LINKS
Walls | -- | Paint, Water-based | Dulux | Dulux, Kitchen & Bath | 50 GY 83/010 White Wing | Off-white | Eggshell | (D6) Painter/Decorator/Installer – First Floor All walls not marked | http://www.dulux.ca Please use Dulux brand primer appropriate for the condition of the surface, preferably the zero VOC Lifemaster.
 | 3 | Wallpaper | Graham & Brown | Dixie | 30-232 | Silver and While | - | (D6) Painter/Decorator/Installer – First Floor Wall ShR1 (See note below) | Paste the wall. Width: 0.52 m Length: 10 m Design match: Straight Pattern repeat: 0.32 m Product info: http://www.grahambrown.ca/us/product/30-232/Dixie%3A+Silver+%26+White+Wallpaper
Ceiling | -- | Paint, Water-based | Dulux | Dulux, Kitchen & Bath | 50 GY 83/010 White Wing | Off-white | Eggshell | - | http://www.dulux.ca Please use Dulux brand primer appropriate for the condition of the surface, preferably the zero VOC Lifemaster.
Woodwork | -- | Paint, Water-based | Dulux | Dulux, Kitchen & Bath | 50 GY 83/010 White Wing | Off-white | Semi-Gloss | - | 
SHOWER ROOM
Note: Walls ShR2, ShR3 and ShR4 in the Shower Room are inside the shower cubicle and are to be covered with Perla shower panels which will be installed by the bathroom contractors before any painting/wallpapering. For details please see Bathroom Installers Specification document.

## Slide 10
TYPE OF SURFACE | PRODUCT DETAILS |  |  |  |  |  |  |  | 
 | Ref ID within room | TYPE | BRAND / SUPPLIER | NAME | CODE / REF | COLOUR | FINISH | REFERENCE DRAWING and WALL IDENTIFIER(S) | ADDITIONAL INFO and WWW LINKS
Walls | -- | Paint, Water-based | Dulux | Dulux, Lifemaster Zero VOC | 40YY 83/021 Minimalist White | Off-white | Eggshell | (D6) Painter/Decorator/Installer – First Floor All walls not marked. | http://www.dulux.ca Please use Dulux brand primer appropriate for the condition of the surface, preferably the zero VOC Lifemaster.
 | 3 | Wallpaper | Mini Moderns | Festival -Stone | N/A | Multi | - | (D6) Painter/Decorator/Installer – First Floor Wall CB1 | Width: 0.52 m Roll length: 10m, 0.52 Repeat – Half Drop Product info: http://www.minimoderns.com/product/festival-wallpaper-stone
Ceiling | -- | Paint, Water-based | Dulux | Dulux, Lifemaster Zero VOC | Ceiling Flat | Standard White (Untinted) | Flat | - | http://www.dulux.ca Please use Dulux brand primer appropriate for the condition of the surface, preferably the zero VOC Lifemaster.
Skirtings | -- | Paint, Water-based | Dulux | Dulux, Lifemaster Zero VOC | 40YY 83/021 Minimalist White | Off-white | Semi-Gloss | - | 
Woodwork | -- | Paint, Water-based | Dulux | Dulux, Lifemaster Zero VOC | 40YY 83/021 Minimalist White | Off-white | Semi-Gloss | - | 
CHILDREN’S BEDROOM

## Slide 11
TYPE OF SURFACE | PRODUCT DETAILS |  |  |  |  |  |  |  | 
 | Ref ID within room | TYPE | BRAND / SUPPLIER | NAME | CODE / REF | COLOUR | FINISH | REFERENCE DRAWING and WALL IDENTIFIER(S) | ADDITIONAL INFO and WWW LINKS
Walls | -- | Paint, Water-based | Dulux | Dulux, Lifemaster Zero VOC | 56BG 81/023 Chilly Morning | Off-white | Eggshell | (D6) Painter/Decorator/Installer – First Floor All walls not marked, and the wall areas of wall GR1 that are not labeled otherwise. | http://www.dulux.ca Please use Dulux brand primer appropriate for the condition of the surface, preferably the zero VOC Lifemaster.
 | 3 | Paint, Water-based | Dulux | Dulux, Lifemaster Zero VOC | 30BG 76/107 Winterscape | Light Teal | Eggshell | (D6) Painter/Decorator/Installer – First Floor Wall GR1-A | 
Ceiling | -- | Paint, Water-based | Dulux | Dulux, Lifemaster Zero VOC | Ceiling Flat | Standard White (Untinted) | Flat | - | 
Skirtings | -- | Paint, Water-based | Dulux | Dulux, Lifemaster Zero VOC | 56BG 81/023 Chilly Morning | Off-white | Semi-Gloss | - | 
Woodwork | -- | Paint, Water-based | Dulux | Dulux, Lifemaster Zero VOC | 56BG 81/023 Chilly Morning | Off-white | Semi-Gloss | - | 
GUEST ROOM

## Slide 12
TYPE OF SURFACE | PRODUCT DETAILS |  |  |  |  |  |  |  | 
 | Ref ID within room | TYPE | BRAND / SUPPLIER | NAME | CODE / REF | COLOUR | FINISH | REFERENCE DRAWING and WALL IDENTIFIER(S) | ADDITIONAL INFO and WWW LINKS
Walls | -- | Paint, Water-based | Dulux | Dulux, Lifemaster Zero VOC | 63GY 83/021 Wish Upon a Star | Off-white | Eggshell | (D6) Painter/Decorator/Installer – First Floor All walls not marked | http://www.dulux.ca Please use Dulux brand primer appropriate for the condition of the surface, preferably the zero VOC Lifemaster.
 | 3 | Wallpaper | Orla Kiely | Small Acorn Cup | 0WALACP501 | Ebony (Black & White) | - | (D6) Painter/Decorator/Installer – First Floor Wall MB1 | Width: 0.52 m Roll length: 10.05 m, Repeat: 17.7 cm Hanging instructions on packaging. Product info: http://www.orlakiely.com/uk.cfm/house/wallpaper/0WALACP501/22070/Ebony/
Ceiling | -- | Paint, Water-based | Dulux | Dulux, Lifemaster Zero VOC | Ceiling Flat | Standard White (Untinted) | Flat | - | http://www.dulux.ca Please use Dulux brand primer appropriate for the condition of the surface, preferably the zero VOC Lifemaster.
Skirtings | -- | Paint, Water-based | Dulux | Dulux, Lifemaster Zero VOC | 63GY 83/021 Wish Upon a Star | Off-white | Semi-Gloss | - | 
Woodwork | -- | Paint, Water-based | Dulux | Dulux, Lifemaster Zero VOC | 63GY 83/021 Wish Upon a Star | Off-white | Semi-Gloss | - | 
MASTER BEDROOM
Note: For the mirrored wall sections as marked on the (D2) Furnishing Layout - First Floor drawing, wardrobe height standard mirrors are to be installed after all other wall and ceiling finishes are applied.
To measure for ordering: (1) Height is to be measured from top edge of skirting to top wardrobe edge. (2) Please obtain exact widths for each of the two sections between the specified wardrobe edges and wall corner / window frame edge, respectively, as marked on the furnishing layout drawing. (Measuring would be best done with the wardrobe already in its proper position.) Please also see (D6) Painter/Decorator/Installer - First Floor drawing for wall sectioning reference.

## Slide 13
TYPE OF SURFACE | PRODUCT DETAILS |  |  |  |  |  |  |  | 
 | Ref ID within room | TYPE | BRAND / SUPPLIER | NAME | CODE / REF | COLOUR | FINISH | REFERENCE DRAWING and WALL IDENTIFIER(S) | ADDITIONAL INFO and WWW LINKS
Walls | -- | Paint, Water-based | Dulux | Dulux, Kitchen & Bath | 30GG 83/013 Winter Walk | Off-white | Eggshell | (D6) Painter/Decorator/Installer – First Floor All walls not marked (See note below) | http://www.dulux.ca Please use Dulux brand primer appropriate for the condition of the surface, preferably the zero VOC Lifemaster.
Ceiling | -- | Paint, Water-based | Dulux | Dulux, Kitchen & Bath | 30GG 83/013 Winter Walk | Off-white | Eggshell | - | 
Woodwork | -- | Paint, Water-based | Dulux | Dulux, Kitchen & Bath | 30GG 83/013 Winter Walk | Off-white | Semi-Gloss | - | 
ENSUITE BATHROOM
Note 1: Walls with IDs EB1 & EB2 in the Ensuite Bathroom are over the bathtub corner and are to be covered with Showerwall panels which are to be installed by the bathroom contractors before any of the paint applications. Please see Bathroom Installers Specification document for details .
Note 2: For the mirrored wall section as marked on the (D2) Furnishing Layout - First Floor drawing, full wall height standard mirror is to be installed after all other wall and ceiling finishes are applied. To measure for ordering: (1) Full wall height is to be measured from top edge of skirting to ceiling; (2) Please obtain an exact width measuring from the towel warmer divider to the projection of the sinks’ front edge onto that wall, as marked on the relevant furnishing layout drawing. Please also see (D6) Painter/Decorator/Installer - First Floor drawing for wall sectioning reference.

## Slide 14
TYPE OF SURFACE | PRODUCT DETAILS |  |  |  |  |  |  |  | 
 | Ref ID within room | TYPE | BRAND / SUPPLIER | NAME | CODE / REF | COLOUR | FINISH | REFERENCE DRAWING and WALL IDENTIFIER(S) | ADDITIONAL INFO and WWW LINKS
Walls | -- | Exterior Paint | Dulux | Diamond Exterior | 30 GY 83/021 Extreme White | Off-white | Satin | (D5) Painter/Decorator/Installer – Ground Floor All walls | http://www.dulux.ca Please use Dulux brand primer appropriate for the condition of the surface, preferably the zero VOC Lifemaster.
Ceiling | -- | Exterior Paint | Dulux | Diamond Exterior | 30 GY 83/021 Extreme White | Off-white | Flat | - | 
Woodwork | -- | Exterior Paint | Dulux | Diamond Exterior | 30 GY 83/021 Extreme White | Off-white | Semi-Gloss | - | 
PATIO

## Slide 15
BALCONY
TYPE OF SURFACE | PRODUCT DETAILS |  |  |  |  |  |  |  | 
 | Ref ID within room | TYPE | BRAND / SUPPLIER | NAME | CODE / REF | COLOUR | FINISH | REFERENCE DRAWING and WALL IDENTIFIER(S) | ADDITIONAL INFO and WWW LINKS
Walls | -- | Exterior Paint | Dulux | Diamond Exterior | 30 GY 83/021 Extreme White | Off-white | Satin | (D6) Painter/Decorator/Installer – First Floor All walls | http://www.dulux.ca Please use Dulux brand primer appropriate for the condition of the surface, preferably the zero VOC Lifemaster.
Ceiling | -- | Exterior Paint | Dulux | Diamond Exterior | 30 GY 83/021 Extreme White | Off-white | Flat | - | 
Woodwork | -- | Exterior Paint | Dulux | Diamond Exterior | 30 GY 83/021 Extreme White | Off-white | Semi-Gloss | - |