## Slide 1
PROJECT DETAILS |  |  |  |  |  |  |  |  | 
NAME: 3-Bedroom Detached House Show Home |  |  |  | SITE ADDRESS: <site address> |  |  |  | CLIENT NAME: <client name> | 
CONTRACTOR DETAILS |  |  |  | 
NAME: <contractor’s name> | ADDRESS: <contractor’s address > | PHONE |  | E-MAIL: <contractor’s e-mail>
 |  | office: <###> | mobile: <###> | 
GENERAL INSTRUCTIONS and PREPATORY NOTES | 
1/ | Please review this specification and schedules and contact me as soon as possible with any issues or questions.
2/ | This specification is organized in a room-by-room format (a separate section is provided for each area).
3/ | Important scheduling note for coordination with the rest of the contractors: All flooring, painting/wallpapering and any other work (ex. any dust creating jobs) that could pose a risk of damaging the window treatments must be completed prior to installing the latter. Please contact me promptly if unsure or about any possible scheduling conflicts.
4/ | Please carry out all work with appropriate care taken so that no damage is inflicted on the newly installed floors and wall coverings.
5/ | No substitutions are to be made unless agreed upon ahead of time.
6/ | The specific manufacturer’s instructions are to be followed in each case.
7/ | As much as possible, please leave the work areas in a tidy fashion at the end of each day. All rubbish is to be promptly removed from the site.
MAIN DETAILS

## Slide 2
HALL, STAIRS AND LANDING
WINDOW APPLICATION |  |  |  | 
MEASUREMENTS (mm) | PRODUCT |  | PLACEMENT | INSTALLATION
 | Ref ID within room | TYPE/NAME |  | 
Window size: Width = 300 Height = 900 Area to be covered / Shade sizing: Width = 200 Height (shade length) = 800 (Recess for inside installation estimated at 200W x 800H) | 12 | Pleated Shades / XL Pleat Firenze | Inside mount. Please follow the detailed manufacturer’s installation instructions. | Detailed instructions by manufacturer: https://static.theshadestore.com/s3/theshadestore/cms/files/TSS_XL_Pleated_Cellular_Install-1.pdf
ADDITIONAL NOTES |  |  |  | 
Widths and heights/lengths determined based on manufacturer’s recommendations. All hardware needed (brackets etc.) is provided with the shade. |  |  |  | 
PRODUCT DETAILS |  |  |  |  |  |  |  | 
Ref ID within room | TYPE/NAME | BRAND/SUPPLIER | QUANTITY | CODE | MATERIAL | COLOUR | OTHER SPECIFICS | WWW
12 | Pleated Shade / XL Pleat Firenze | The Shade Store | 1 | N/A | Firenze, 100% Polyester | White | Unlined Shade size: Width = 200 mm Length = 800 mm Mount type: Inside Control type: Continuous Loop Control position: Right Top-Down-Bottom-Up Feature | Product Info: https://www.theshadestore.com/window-treatments/product/xl-pleated-shade (Please see Firenze)

## Slide 3
STUDY
WINDOW APPLICATION |  |  |  | 
MEASUREMENTS (mm) | PRODUCT |  | PLACEMENT | INSTALLATION
 | Ref ID within room | TYPE/NAME |  | 
Window size: Width = 1200 Height = 900 Area to be covered / Shade sizing: Width = 1260 (added width to minimize light seepage: 1200 + 60) Height (shade length) = 960 (added height/length for outside mount: 900 + 60) | 21 | Pleated Shades / XL Pleat Firenze | Outside mount. Please follow the detailed manufacturer’s installation instructions. Please place shade so that the added width and length are divided equally between top – bottom and left – right sides, respectively. | Detailed instructions by manufacturer: https://static.theshadestore.com/s3/theshadestore/cms/files/TSS_XL_Pleated_Cellular_Install-1.pdf
ADDITIONAL NOTES |  |  |  | 
Widths and heights/lengths determined based on manufacturer’s recommendations. All hardware needed (brackets etc.) is provided with the shade. |  |  |  | 
PRODUCT DETAILS |  |  |  |  |  |  |  | 
Ref ID within room | TYPE/NAME | BRAND/SUPPLIER | QUANTITY | CODE | MATERIAL | COLOUR | OTHER SPECIFICS | WWW
21 | Pleated Shade / XL Pleat Firenze | The Shade Store | 1 | N/A | Firenze, 100% Polyester | White | Unlined Shade size: Width = 1260 mm Length = 960 mm Mount type: Outside Control type: Continuous Loop Control position: Left Top-Down-Bottom-Up Feature | Product Info: https://www.theshadestore.com/window-treatments/product/xl-pleated-shade (Please see Firenze)

## Slide 4
DOWNSTAIRS BATHROOM
WINDOW APPLICATION |  |  |  | 
MEASUREMENTS (mm) | PRODUCT |  | PLACEMENT | INSTALLATION
 | Ref ID within room | TYPE/NAME |  | 
Window size: Width = 900 Height = 900 Area to be covered / Shade sizing: Same as window size. | 19 | Interior Shutters / Eclipse Plantation Shutters | Outside the frame. Please follow the detailed manufacturer’s installation instructions. | Detailed instructions by manufacturer: http://www.eclipseshutters.com/pdfs/Eclipse_Installation_2011.pdf
ADDITIONAL NOTES |  |  |  | 
All hardware needed (brackets etc.) is provided with the shutters. For a list of tools and additional items required for the installation please see the installation instructions. |  |  |  | 
PRODUCT DETAILS |  |  |  |  |  |  |  | 
Ref ID within room | TYPE/NAME | BRAND/SUPPLIER | QUANTITY | CODE | MATERIAL | COLOUR | OTHER SPECIFICS | WWW
19 | Interior Shutters / Eclipse Plantation Shutters | Eclipse Shutters | 1 frame with 2 panels | N/A | Vinyl | Cotton | Clearview hidden tilt-bar Louvers size: 4.5 inch (114.3 mm) Standard hinge system, individually hinged panels | Product Info: http://www.eclipseshutters.com/45-inch-plantation-shutters.html

## Slide 5
SITTING ROOM
PRODUCT DETAILS |  |  |  |  |  |  |  | 
Ref ID within room | TYPE/NAME | BRAND/SUPPLIER | QUANTITY | CODE | MATERIAL | COLOUR | OTHER SPECIFICS | WWW
29 | Pleated Shade / XL Pleat Firenze | The Shade Store | 2 (one for each of the two identical windows) | N/A | Firenze, 100% Polyester | White | Blackout lining, white Shade size: Width = 1260 mm Length = 960 mm Mount type: Outside Control type: Continuous Loop Control position: Left Top-Down-Bottom-Up Feature | Product Info: https://www.theshadestore.com/window-treatments/product/xl-pleated-shade (Please see Firenze)
WINDOW APPLICATION (This table to be used for each of the two identical windows sized 1200 mm x 900 mm) |  |  |  | 
MEASUREMENTS (mm) | PRODUCT |  | PLACEMENT | INSTALLATION
 | Ref ID within room | TYPE/NAME |  | 
Window size: Width = 1200 Height = 900 Area to be covered / Shade sizing: Width = 1260 (added width to minimize light seepage: 1200 + 60) Height (shade length) = 960 (added height/length for outside mount: 900 + 60) | 29 | Pleated Shades / XL Pleat Firenze | Outside mount. Please follow the detailed manufacturer’s installation instructions. Please place shade so that the added width and length are divided equally between top – bottom and left – right sides, respectively. | Detailed instructions by manufacturer: https://static.theshadestore.com/s3/theshadestore/cms/files/TSS_XL_Pleated_Cellular_Install-1.pdf
ADDITIONAL NOTES |  |  |  | 
Widths and heights/lengths determined based on manufacturer’s recommendations. All hardware needed (brackets etc.) is provided with the shade. |  |  |  | 

## Slide 6
PLAYROOM
WINDOW APPLICATION |  |  |  | 
MEASUREMENTS (mm) | PRODUCT |  | PLACEMENT | INSTALLATION
 | Ref ID within room | TYPE/NAME |  | 
Window size: Width = 1200 Height = 900 Area to be covered / Shade sizing: Width = 1260 (added width to minimize light seepage: 1200 + 60) Height (shade length) = 960 (added height/length for outside mount: 900 + 60) | 19 | Pleated Shades / XL Pleat Firenze | Outside mount. Please follow the detailed manufacturer’s installation instructions. Please place shade so that the added width and length are divided equally between top – bottom and left – right sides, respectively. | Detailed instructions by manufacturer: https://static.theshadestore.com/s3/theshadestore/cms/files/TSS_XL_Pleated_Cellular_Install-1.pdf
ADDITIONAL NOTES |  |  |  | 
Widths and heights/lengths determined based on manufacturer’s recommendations. All hardware needed (brackets etc.) is provided with the shade. |  |  |  | 
PRODUCT DETAILS |  |  |  |  |  |  |  | 
Ref ID within room | TYPE/NAME | BRAND/SUPPLIER | QUANTITY | CODE | MATERIAL | COLOUR | OTHER SPECIFICS | WWW
19 | Pleated Shade / XL Pleat Firenze | The Shade Store | 1 | N/A | Firenze, 100% Polyester | White | Unlined Shade size: Width = 1260 mm Length = 960 mm Mount type: Outside Control type: Cordless Top-Down-Bottom-Up Feature | Product Info: https://www.theshadestore.com/window-treatments/product/xl-pleated-shade (Please see Firenze)

## Slide 7
DINING ROOM
PRODUCT DETAILS |  |  |  |  |  |  |  | 
Ref ID within room | TYPE/NAME | BRAND/SUPPLIER | QUANTITY | CODE | MATERIAL | COLOUR | OTHER SPECIFICS | WWW
17 | Pleated Shade / XL Pleat Firenze | The Shade Store | 2 | N/A | Firenze, 100% Polyester | White | Unlined Shade size: Width = 1260 mm Length = 960 mm Mount type: Outside Control type: Continuous Loop Control position: Left Top-Down-Bottom-Up Feature | Product Info: https://www.theshadestore.com/window-treatments/product/xl-pleated-shade (Please see Firenze)
17 | Pleated Shade / XL Pleat Firenze | The Shade Store | 1 | N/A | Firenze, 100% Polyester | White | Unlined Shade size: Width = 1860 mm Length = 960 mm Mount type: Outside Control type: Continuous Loop Control position: Left Top-Down-Bottom-Up Feature | 
Section 7 Dining Room continued on next page….

## Slide 8
DINING ROOM - continued
WINDOW APPLICATION (Application #1 of Product #1 is to be used for each of the two identical windows sized 1200 mm x 900 mm, Application #2 of Product #2 is to be used for the window sized 1800 mm x 900 mm) |  |  |  |  | 
# | MEASUREMENTS (mm) | PRODUCT |  | PLACEMENT | INSTALLATION
 |  | Ref ID within room | TYPE/NAME |  | 
1 | Window size: Width = 1200 Height = 900 Area to be covered / Shade sizing: Width = 1260 (added width to minimize light seepage: 1200 + 60) Height (shade length) = 960 (added height/length for outside mount: 900 + 60) | 17 | Pleated Shades / XL Pleat Firenze | Outside mount. Please follow the detailed manufacturer’s installation instructions. Please place shade so that the added width and length are divided equally between top – bottom and left – right sides, respectively. | Detailed instructions by manufacturer: https://static.theshadestore.com/s3/theshadestore/cms/files/TSS_XL_Pleated_Cellular_Install-1.pdf
2 | Window size: Width = 1800 Height = 900 Area to be covered / Shade sizing: Width = 1860 (added width to minimize light seepage: 1800 + 60) Height (shade length) = 960 (added height/length for outside mount: 900 + 60) | 17 | Pleated Shades / XL Pleat Firenze | Outside mount. Please follow the detailed manufacturer’s installation instructions. Please place shade so that the added width and length are divided equally between top – bottom and left – right sides, respectively. | Detailed instructions by manufacturer: https://static.theshadestore.com/s3/theshadestore/cms/files/TSS_XL_Pleated_Cellular_Install-1.pdf
ADDITIONAL NOTES |  |  |  |  | 
Widths and heights/lengths determined based on manufacturer’s recommendations. All hardware needed (brackets etc.) is provided with the shade. |  |  |  |  | 

## Slide 9
KITCHEN
PRODUCT DETAILS |  |  |  |  |  |  |  | 
Ref ID within room | TYPE/NAME | BRAND/SUPPLIER | QUANTITY | CODE | MATERIAL | COLOUR | OTHER SPECIFICS | WWW
31 | Venetian Blinds / CB Metal Venetian Blind | Crosby Blinds | 1 | N/A | Alumunium | Mirror Chrome | Slat size: 25 mm Raise control: left Tilt control: right Colour coordinated head and bottom rails, cords Blind size: Width = 1200 mm Length = 900 mm Mount type: inside recess, top fix | Product Info: http://www.crosbyblinds.co.uk/shop/cb-premier-blinds/metal-venetian-blinds/cb-metal-venetian-blinds (Please see Mirror Chrome)
31 | Venetian Blinds / CB Metal Venetian Blind | Crosby Blinds | 1 | N/A | Alumunium | Mirror Chrome | Slat size: 25 mm Raise control: left Tilt control: right Colour coordinated head and bottom rails, cords Blind size: Width = 850 mm Length = 900 mm Mount type: inside recess, top fix | 
Section 8 Kitchen continued on next page….

## Slide 10
KITCHEN - continued
WINDOW APPLICATION |  |  |  |  | 
# | MEASUREMENTS (mm) | PRODUCT |  | PLACEMENT | INSTALLATION
 |  | Ref ID within room | TYPE/NAME |  | 
1 | Window size: Width = 1200 Height = 900 Area to be covered / Shade sizing: Width = 1200 Height (shade length) = 900 (Sized for inside recess mount, window recess estimated the same as window size.) | 31 | Venetian Blinds / CB Metal Venetian Blind | Inside recess mount, top fix. Please follow the detailed manufacturer’s installation instructions. | Detailed instructions by manufacturer: http://www.blindshouse.co.uk/resources/uploads/files/howtofitvenetianblinds.pdf
2 | Window size: Width = 850 Height = 900 Area to be covered / Shade sizing: Width = 850 Height (shade length) = 900 (Sized for inside recess mount, window recess estimated the same as window size.) | 31 | Venetian Blinds / CB Metal Venetian Blind | Inside recess mount, top fix. Please follow the detailed manufacturer’s installation instructions. | Detailed instructions by manufacturer: http://www.blindshouse.co.uk/resources/uploads/files/howtofitvenetianblinds.pdf
ADDITIONAL NOTES |  |  |  |  | 
Widths and heights/lengths determined based on manufacturer’s recommendations. All hardware needed (brackets etc.) is provided with the blind. |  |  |  |  | 

## Slide 11
SHOWER ROOM
WINDOW APPLICATION |  |  |  | 
MEASUREMENTS (mm) | PRODUCT |  | PLACEMENT | INSTALLATION
 | Ref ID within room | TYPE/NAME |  | 
Window size: Width = 1200 Height = 900 Area to be covered / Shade sizing: Same as window size. | 22 | Interior Shutters / Eclipse Plantation Shutters | Outside the frame. Please follow the detailed manufacturer’s installation instructions. | Detailed instructions by manufacturer: http://www.eclipseshutters.com/pdfs/Eclipse_Installation_2011.pdf
ADDITIONAL NOTES |  |  |  | 
All hardware needed (brackets etc.) is provided with the shutters. For a list of tools and additional items required for the installation please see the installation instructions. |  |  |  | 
PRODUCT DETAILS |  |  |  |  |  |  |  | 
Ref ID within room | TYPE/NAME | BRAND/SUPPLIER | QUANTITY | CODE | MATERIAL | COLOUR | OTHER SPECIFICS | WWW
22 | Interior Shutters / Eclipse Plantation Shutters | Eclipse Shutters | 1 frame with 2 panels | N/A | Vinyl | Cotton | Clearview hidden tilt-bar Louvers size: 4.5 inch (114.3 mm) Standard hinge system, individually hinged panels | Product Info: http://www.eclipseshutters.com/45-inch-plantation-shutters.html

## Slide 12
CHILDREN’S BEDROOM
WINDOW APPLICATION |  |  |  | 
MEASUREMENTS (mm) | PRODUCT |  | PLACEMENT | INSTALLATION
 | Ref ID within room | TYPE/NAME |  | 
Window size: Width = 1200 Height = 900 Area to be covered / Shade sizing: Width = 1260 (added width to minimize light seepage: 1200 + 60) Height (shade length) = 960 (added height/length for outside mount: 900 + 60) | 20 | Pleated Shades / XL Pleat Firenze | Outside mount. Please follow the detailed manufacturer’s installation instructions. Please place shade so that the added width and length are divided equally between top – bottom and left – right sides, respectively. | Detailed instructions by manufacturer: https://static.theshadestore.com/s3/theshadestore/cms/files/TSS_XL_Pleated_Cellular_Install-1.pdf
ADDITIONAL NOTES |  |  |  | 
Widths and heights/lengths determined based on manufacturer’s recommendations. All hardware needed (brackets etc.) is provided with the shade. |  |  |  | 
PRODUCT DETAILS |  |  |  |  |  |  |  | 
Ref ID within room | TYPE/NAME | BRAND/SUPPLIER | QUANTITY | CODE | MATERIAL | COLOUR | OTHER SPECIFICS | WWW
20 | Pleated Shade / XL Pleat Firenze | The Shade Store | 1 | N/A | Firenze, 100% Polyester | White | Blackout lining, white Shade size: Width = 1260 mm Length = 960 mm Mount type: Outside Control type: Cordless Top-Down-Bottom-Up Feature | Product Info: https://www.theshadestore.com/window-treatments/product/xl-pleated-shade (Please see Firenze)

## Slide 13
GUEST ROOM
WINDOW APPLICATION |  |  |  | 
MEASUREMENTS (mm) | PRODUCT |  | PLACEMENT | INSTALLATION
 | Ref ID within room | TYPE/NAME |  | 
Window size: Width = 1200 Height = 900 Area to be covered / Shade sizing: Width = 1260 (added width to minimize light seepage: 1200 + 60) Height (shade length) = 960 (added height/length for outside mount: 900 + 60) | 21 | Pleated Shades / XL Pleat Firenze | Outside mount. Please follow the detailed manufacturer’s installation instructions. Please place shade so that the added width and length are divided equally between top – bottom and left – right sides, respectively. | Detailed instructions by manufacturer: https://static.theshadestore.com/s3/theshadestore/cms/files/TSS_XL_Pleated_Cellular_Install-1.pdf
ADDITIONAL NOTES |  |  |  | 
Widths and heights/lengths determined based on manufacturer’s recommendations. All hardware needed (brackets etc.) is provided with the shade. |  |  |  | 
PRODUCT DETAILS |  |  |  |  |  |  |  | 
Ref ID within room | TYPE/NAME | BRAND/SUPPLIER | QUANTITY | CODE | MATERIAL | COLOUR | OTHER SPECIFICS | WWW
21 | Pleated Shade / XL Pleat Firenze | The Shade Store | 1 | N/A | Firenze, 100% Polyester | White | Blackout lining, white Shade size: Width = 1260 mm Length = 960 mm Mount type: Outside Control type: Continuous Loop Control position: Left Top-Down-Bottom-Up Feature | Product Info: https://www.theshadestore.com/window-treatments/product/xl-pleated-shade (Please see Firenze)

## Slide 14
MASTER BEDROOM
PRODUCT DETAILS |  |  |  |  |  |  |  | 
Ref ID within room | TYPE/NAME | BRAND/SUPPLIER | QUANTITY | CODE | MATERIAL | COLOUR | OTHER SPECIFICS | WWW
28 | Ripple Fold Draperies – Blackout Cottons | The Shade Store | 2 equal panles | N/A | Cotton Sateen, 100% combed cotton | White (A); Leading edge decorative border in Black (B) | Decorative borders: 4” leading edge Cotton Sateen in Black Blackout lining, white Fabric returns to be customized to 254 mm [10”] Total drapery size (to be divided into 2 equal panels [1 left, 1 right]): Width = 4760 mm Length = 2356 mm Mount type: Ceiling Custom track included (to be mounted on the outside, furthest from windows) Control type: Cord | Product Info: https://www.theshadestore.com/window-treatments/product/ripple-fold-drapery (See Cotton Sateen)
29 | Ripple Fold Draperies – Sheers | The Shade Store | 2 equal panels | N/A | Batiste sheers, 100% polyester | White | Unlined Fabric returns: standard 101.6 mm [4”] Total drapery size (to be divided into 2 equal panels [1 left, 1 right]): Width = 4760 mm Length = 2356 mm Mount type: Ceiling Custom track included (to be mounted on the inside, closest to windows) Control type: Cord | Product Info: https://www.theshadestore.com/window-treatments/product/ripple-fold-drapery (See Batiste Sheers)
Section 12 Master Bedroom continued on next page….

## Slide 15
MASTER BEDROOM - continued
WINDOW APPLICATION |  |  |  | 
MEASUREMENTS (mm) | PRODUCT |  | PLACEMENT | INSTALLATION
 | Ref ID within room | TYPE/NAME |  | 
2 Windows, each sized: Width = 1800 Height = 900 Area to be covered / Drapes sizing: To include both windows and the balcony door (W900) that separates them: Width = 4760 (added width to allow for drapes to stackback: 4500 + 260) Height (drapes length) = 2356 { Rounded up from this calculation: 2400 (full ceiling height) – 31.75 [1 ¼ “] (height from top of track to drapery top edge) – 12.7 [½ “] (clearance from floor for ease of frequent opening and closing of draperies) } | 28 | Ripple Fold Draperies – Blackout Cottons | Ceiling mount on the outside track (furthest from windows). The outside track is to be mounted to accommodate the maximum drape projection of 228.6 mm [9”] which is to include 2 x S-curve widths of 101.6 mm [4”] + 25.4 mm [1”] of space between the 2 draperies for movement. Please see Custom Track installation instructions for more details. A pair of two equal panels will be hung. Fabric returns customized to 254 mm [10”]. | Detailed instructions by manufacturer: Custom track installation: https://static.theshadestore.com/s3/theshadestore/cms/files/TSS_Custom_Track_Install.pdf Ripple Fold Drapery Installation: https://static.theshadestore.com/s3/theshadestore/cms/files/TSS_Ripple_Fold_Install.pdf
 | 29 | Ripple Fold Draperies – Sheers | Ceiling mount on the inside track (closest to windows). Track projection should be adjusted appropriately to allow enough space for the S-curve of the ripple fold draperies which is 101.6 mm (4”) front to back. Please see Custom Track installation instructions for more details. A pair of two equal panels will be hung. Fabric returns: standard 101.6 mm [4”]. | 
ADDITIONAL NOTES |  |  |  | 
Widths and heights/lengths determined based on manufacturer’s recommendations. Two custom tracks are to be used for this installation in order to layer the two types of draperies. |  |  |  | 

## Slide 16
ENSUITE BATHROOM
WINDOW APPLICATION |  |  |  | 
MEASUREMENTS (mm) | PRODUCT |  | PLACEMENT | INSTALLATION
 | Ref ID within room | TYPE/NAME |  | 
Window size: Width = 1200 Height = 900 Area to be covered / Shade sizing: Same as window size. | 20 | Interior Shutters / Eclipse Plantation Shutters | Outside the frame. Please follow the detailed manufacturer’s installation instructions. | Detailed instructions by manufacturer: http://www.eclipseshutters.com/pdfs/Eclipse_Installation_2011.pdf
ADDITIONAL NOTES |  |  |  | 
All hardware needed (brackets etc.) is provided with the shutters. For a list of tools and additional items required for the installation please see the installation instructions. |  |  |  | 
PRODUCT DETAILS |  |  |  |  |  |  |  | 
Ref ID within room | TYPE/NAME | BRAND/SUPPLIER | QUANTITY | CODE | MATERIAL | COLOUR | OTHER SPECIFICS | WWW
20 | Interior Shutters / Eclipse Plantation Shutters | Eclipse Shutters | 1 frame with 2 panels | N/A | Vinyl | Cotton | Clearview hidden tilt-bar Louvers size: 4.5 inch (114.3 mm) Standard hinge system, individually hinged panels | Product Info: http://www.eclipseshutters.com/45-inch-plantation-shutters.html